## Slide 1: Using an Orienteering Compass
By Monica Spicker
2008

## Slide 2: Objectives
Identify types and parts of a compass
Determine a direction from a map.
Transfer a reading onto a map
Follow a reading in the field
Take a reading in the field
Determine position by resectioning in the field.

## Slide 3: Compass styles Azimuth Bearing

## Slide 4: Compass parts
From
To
Needle “Red Fred”
Base lines
Screw to set declination: No further calculations needed!
Reading taken or set here
Orienting arrow. The “Shed”

## Slide 5: Magnetic vs True North

## Slide 6: Magnetic Declination
Compass needle points to magnetic north
Maps oriented to true north
Difference must be calculated or preset on the compass itself.
True reading (map) = magnetic (needle) + dec
By convention east is always + and west is –
MEAT: Magnetic East Add True

## Slide 7: My compass cannot be set for declination!
Make plans to buy one.
OR Can draw lines of magnetic north onto your map to align your compass, rather than using true north (must change every so often or buy a new map)
OR Can draw a line at the magnetic north position on your compass.
  If true (map reading) is on the dial, rotate that reading to the declination mark, and you have set magnetic to follow in the field.
  If magnetic is on the dial (field reading), then the reading at the declination mark is the true reading. Rotate that reading to the dial to plot lines on your map.
  Needs to be changed regularly, but easier than on the map.

## Slide 8: Grid North
The angle at which the UTM grid is oriented.
UTM grid lines may be too far off for orienting the compass!

## Slide 9: Determining Direction
Need a map
Best if there are grid lines that run north-south on it
Compass
The objective is to determine the setting needed to travel from Point A to Point B in the field.

## Slide 10: Determining Direction: Step 1
From Lost Lake
To this campground
From
To
Compass edge is used like a ruler

## Slide 11: Step 2
Turn dial so BASE lines are parallel to true north. N of dial must point north.
(Red orienting arrow is skewed, because declination is set. )
IGNORE THE NEEDLE!
Read direction here. No further calculations needed! Leave this reading set, if you want to travel this route.

## Slide 12: Practice

## Slide 13: Following a Set Direction: Step 1
Set the desired reading here

## Slide 14: Following a Set Direction: Step 2
Turn yourself until “Red Fred is in the Shed” (The red needle is inside the outline arrow in the base plate.)

## Slide 15: Step 3: Following a Set Direction
Hold the compass LEVEL in front of you.
Flip the mirror down so you see the dial in it.
The black line in the mirror should appear to go through the reading.
The sighting notch in the black cover points to your target.
Repeat when you reach your first target until you reach your target. Count paces as needed.
Make sure Red Fred is still in the shed!

## Slide 16: Resectioning
Intersection of two line features to determine position.
  Road and elevation
  Creek and road
  One or more directions drawn on map and another line feature.

## Slide 17: Resectioning Examples
Intersection of 2 trails
Intersection of trail and stream
Intersection of stream and elevation 11400

## Slide 18: Resectioning with compass directions
A
B
Your Location in Field
X
Take compass readings on two prominent landmarks (A and B) that you can identify on a map.
Plot these on the map. Intersection is your position.

## Slide 19: Taking a Reading
Hold compass level in front of you
Flip down the mirror until you can see the dial.
Aim the sighting notch in the compass at the target
Turn the dial until Red Fred is in the Shed
The direction is read at the hinge end of the dial.
Look at target

## Slide 20: Plotting a Direction: Step 1
Set heading on compass
TO: If you shot to a known point, lay this end over that point on the map
FROM: If you shot from a known point, then lay this end over the point on the map
Compass edge acts like a ruler

## Slide 21: Plotting a Direction: Step 2
1) Turn entire compass until base lines are parallel with true north on map and the N on the dial is north
2) Draw line along compass edge

## Slide 22: Step 3
For resectioning, repeat with a second line feature or second compass reading
Intersection is your location.
Lost Lake is now found!
If plotting a distance from a known point, mark off the distance to see the objective.

## Slide 23: Plotting Practice

## Slide 24: Field Practice