## Slide 1: Maps: An Overview
By Monica Spicker
2012

## Slide 2: Objectives
Identify different types of maps
Identify elements of maps
Use scale ratio and scale bar to determine distance
Identify terrain features from contours
Determine elevation
Match map features to real features in the field.
Identify hazardous slopes via contours by aspect, shape and steepness.

## Slide 3: Types of Maps
Planimetric
  Flat surface – no geographic features
  Road maps, ownership maps, tourist maps.
Topographic
  Terrain represented via contour lines
  Other geographic features such as rivers, seasonal creeks, permanent snowfields, vegetation, etc.

## Slide 4: Elements of Maps
North
  True
  Magnetic
  Grid
Scale
  Scale bar
  Scale ratio
    1 ruler unit on map = RF ruler units on the ground
    1: 24000 means 1 map inch = 24000 ground inches
    or 1 map cm = 24000 ground cm.
    Need to convert ratio ruler units to ground units or ground units to map inches to use correctly!

## Slide 5: Elements of Maps (part 1)
Legend
  Not all symbols mean the same thing
  Certain cultural biases
Grid systems
  Alphanumeric
  Public Land Survey System (PLSS or “legals”)
  Geographic (Latitude/Longitude)
  Universal Transverse Mercator (UTM)

## Slide 6: Elements of Maps (part 2)
Date
  A map is a snapshot in time.
Datum
  Essential for GPS use – will discuss later
Contour Interval
  Needed to determine elevations on a topographic map and to assess steepness.
General area of map
  The bigger picture

## Slide 7: Finding Distances

## Slide 8: Using the Scale Bar
Use a string (careful not to stretch), paper edge, chain or special wheel to determine total length of trail, road, feature, etc.
Lay down against the scale bar to determine total distance.
Be careful of where 0 is on the scale bar!
About 750 meters

## Slide 9: Using the Scale Ratio
Decide map units (ruler units) you will be using: inches or cm
Convert the RF to the desired ground units (usually feet, miles, meters or kilometers) based on the ruler units to be used.
Measure the distance on the map and multiply by the converted RF for total distance.
Example: Scale ratio = 1:10000. Will measure in cm and want the distance in meters.
  10000/100 cm per meter = 100 m.
  Measure a road that is 5.3 cm long.
  5.3 * 100 = 530 m of road.

## Slide 10: Measuring Distance in the Field
Time – hard to estimate unless well practiced
Pacing – also takes practice.
  1 pace = 2 steps
  Changes with conditions, terrain and footwear
  Know pace in terms of meters or feet
  Pace out intervals not entire distance
  Use pacing beads to keep track.
  On team maneuvers, common to use one person as pacer and another to run compass.
  Should be able to do both compass and pace work.
Example: Want to go 970 meters.
  Pace is 60 paces per 100 meters.
  Pace out 100 meters 9 times, keeping track with pacing beads each time complete 100 meters.
  Pace final 70 meters to objective.

## Slide 11: Some map and scale exercises!

## Slide 12: Understanding contour maps.

## Slide 13: A portion of a contour map
Viewpt

## Slide 14: 3-D Version of the same map

## Slide 15: The Real Thing

## Slide 16: What are contour lines?
Lines of equal elevation.
Brown on land, blue on glaciers and snow fields.
Every fifth line darker, many are labeled.
  primary contour.
Four lighter lines between
Change in elevation between any two lines: contour interval (elevation change).
Difference in elevation between 2 primaries divided by 5 = contour interval.
39 foot cliffs can hide between 40 ft intervals!
“Flat” trails can rise and fall.
What is the contour interval?

## Slide 17: Determining elevations
Some points have labeled elevations
Points between contour lines are interpolated (usual to estimate at ½ interval)
Benchmark
Surveyed point; temporary
Spot elevation

## Slide 18: Determining elevations in the field
Barometric altimeter
  Analog
  Digital
  Must be reset often
  Sensitive to weather
GPS
  Computed elevation can be off because of the Earth model used.
  Some GPS also have barometric altimeters.

## Slide 19: Features Shown by Contours – Example 1
Steep
Flat
Trail
Viewpt
Forested
No trees

## Slide 20: 3-D Version of the same map – Example 1
Steep
Flat
Trail
Forested
No trees

## Slide 21: Google Earth image
Are all the places indicated on the map as forested still forested?
This is why map date is important!

## Slide 22: Google Earth 3-D image

## Slide 23: Photo taken Dec 2011

## Slide 24: A comparison between a topographic map and a picture of the same location

## Slide 25: Slope features
Hilltop – full circle
Draws & Creeks:
Point uphill,
usually sharp.
Saddle
2 contours bend away
Ridge:
“point” downhill, usually rounded.

## Slide 26: Features Shown by Contours – Example 2
Hilltop
Ridge
Saddle
Seasonal Creek
Draw or gully
Viewpt

## Slide 27: 3-D Version of the same map – Example 2
Saddle
Ridge
Hilltop
Seasonal Creek
Draw or gully
Notes: View is different from the pictures because when you look at the contours backwards, i.e., from the south, the ridges and gullies invert!

## Slide 28: Match the contours to the features! Vegetation can obscure features.

## Slide 29: Contours matched to features

## Slide 30: Practice with contours

## Slide 31: Slope Aspect: which direction a slope faces
Draw arrow perpendicular to contours and down hill (Fall Line).
That direction is the aspect!
S
N
W
E

## Slide 32: Using compass to measure aspect in the field
  Face away from the hill (back to the hill)
  Hold compass in front of you and rotate dial until “Red Fred” (the needle) in in the “Shed” (red outline arrow in base plate).
  Reading at hinge is the aspect. (in this case W, SW)

## Slide 33: Slope Shape
These patterns are typical of avalanche paths!
Convex slope: flat on top, steeper towards the bottom.
Concave slope: Steeper at top, flatter towards the bottom.

## Slide 34: Slope Shape (3-d)
Convex
Concave
Possible avalanche paths

## Slide 35: Dangerous Slopes
Most avalanches occur on 25 to 45 degree slopes.
N and NE aspects are more avalanche prone in midwinter; S and SW slopes in spring.
Prevailing winds are from the SW: NE slopes are leeward and loading areas.
Convex slopes more dangerous than concave.

## Slide 36: Slope angle
Fall Line: line perpendicular to the contours.
Depends on contour interval and map scale:
  1:24000, 40 foot contour
    20º: 19 contours per inch
    30º: 29 contours per inch
    40º: 42 contours per inch
    Use grid

## Slide 37: Slope angle: Using the Grid

## Slide 38: Using compass to measure slope in the field
Dial compass to west at the hinge.
Hold compass at same angle as the slope, with the declination scale at the bottom.
Where the black swinging needle points is your slope angle in degrees.
(in this case 27º)

## Slide 39: More contour and elevation exercises.