## Slide 1: Using Terrain Navigator Pro
Recommendation
Download the demo version of TN Pro and use it to practice the basic skills presented in this lesson.
http://www.maptech.com/support/downloads.cfm
Monica Spicker
2008

## Slide 2: Start Up – First Choice

## Slide 3: Start Up – Second Choice
Find a place name within a category.

## Slide 4: Start Up – Third Choice
New Map CD
  MUST have registration number!

## Slide 5: Main Screen
Notes: Point out: Coordinates, Datum, Pan, Zoom in Zoom Out.

## Slide 6: Help
F1 key will bring up index to Help at any time.
Type in key word if you get stuck.

## Slide 7: Set up
Check each time!
Unless changed, setup will automatically saved.
Notes: Coordinates and GPS a must.
Custom Grid is nice to have.

## Slide 8: Set up (2)
  UTM
  NAD83 or WGS84

## Slide 9: Set Up (3)
GPS
  Select manufacturer
  Select model
  Select port
  Test connection!
  Some GPS need drivers installed beforehand! Check each person’s GPS

## Slide 10: Set up (4)
Custom Grid
  Will be printed, if with gridlines is selected!

## Slide 11: Layer Visibility
All markers, tracks, custom grids are termed as layers.
Can be turned on and off.
Will print only if visibility is on!
Turns all layers on and off

## Slide 12: 3D View
Notes: First zoom in to desired scale, then can use various sliders or the pan hand to change elevation and view angle.

## Slide 13: Find Coordinates

## Slide 14: Setting and Editing Markers
Select marker tool, then click on spot to mark.
Put pan hand over marker and right click to generate options menu.
Edit name, symbol, color, etc. as needed.

## Slide 15: Drawing Tracks
Select track tool.
Click on starting point, click at each turning point (do not trace).
If the track is to be a closed area, stop just short of the beginning.
Right click, select finish track.
If the track is a closed area, point to it, right click and toggle loop to automatically close it.
Track length is always displayed.

## Slide 16: Track Editing & Information
Edit: name, color, font, label, etc.
Information: will give you area
Delete
Profile: side view to see amount of elevation gain and loss.
Line of Sight: shows obstructions between the endpoints of a track.
  Draw a line between team locations or to command and finish track. If the distance is greater than 2 to 3 miles, FRS may not not reach.
  If a hill is on the line of sight, FRS radio use will be hampered.
Send to GPS: GPS must be connected and turned on before using this feature.

## Slide 17: Find Tracks and Markers

## Slide 18: Bookmarks
A specific map view, including scale, can be saved as a bookmark. Go to View,
  Can edit the name, etc.
Find will then relocate that view as needed.
  Good for large area & multiple teams

## Slide 19: Printing
Set Scale (not %), Print Quality, turn on Layers, Rulers, With gridlines, and Scale Bar. Only visible layers will be printed.
Make sure the blue box is centered over what you want to print!

## Slide 20: Export
Save (archive) current set of layers - .tpa
Multiple markers, tracks and routes as separate files.
Pay attention where you are storing them!!!

## Slide 21: Export Tips
If you are creating tracks and routes on one computer but may have to switch to another, it is a good idea to save your work as separate layers (safest) or as a project archive.
The saved files can then be imported to another computer that has TN Pro.
The other types of export formats are for importing into other software packages.
Pay attention where you are storing them!!!
  Keep everything related to a project in one folder.
  Easy to transfer to a flashdrive or disk.

## Slide 22: Import
Open previously saved (exported or archived) projects, tracks, routes, markers, etc.
  Base map must first be loaded.
Will only import .txf (Track Export File) and .mxf (Marker Export File) and .tpa (Terrain Project Archive) formats.
Exported track and marker files can be read by older versions of Terrain Navigator.
When importing a project, you will have to give it a new name.
Need to know where they have been stored!

## Slide 23: GPS
Some of these features are for using TN Pro real time with a receiver.
Most often will use Send, Receive and Setup
1. Connect GPS receiver to port via its cable
2. Turn on Receiver
3. Select Receive or Send and with what you are working
(waypoints [markers], tracks or routes.)

## Slide 24: GPS files
Downloaded files are treated by TN Pro like drawn markers or tracks.
Can be exported (saved)
Can be uploaded to other GPS units.
Drawn markers and tracks can be uploaded
Change set up if using a variety of receivers.
May want to work with all of one type of receiver before switching to another.