## Slide 1: Grid-edge Modeling and Optimization to support Decarbonization and Resilience
Presenter: Anamika Dubey
Huie-Rogers Endowed Chair
Associate Professor of Electrical Engineering
Washington State University, Pullman
Co-director, PNNL/WSU AGI
Research Scientist, Pacific Northwest National Lab (PNNL)
(anamika.dubey@wsu.edu)
PNNL/WSU Advanced Grid Institute (AGI)
AGI Day 2024
Date: 8/28/2024
Email: anamika.dubey@wsu.edu
Website: anamika-dubey.github.io

## Slide 2
Active Electric Power Distributions Systems: Decarbonization and Electrification
  Very-large penetration of distributed energy resources – 4.2 million homes installed solar panels as of 2024
Lack of active management of these resources  underutilized infrastructure
(Active grid management  Distribution and Grid-edge Optimization/Control)
Economywide electrification (including transportation) could increase U.S. electricity consumption by up to 38% by 2050.
Dramatic increase of extreme event related outages: predominant cause of outages are damages at MV/LV level
Number of outages affecting more than 50k customers

## Slide 3
Active Electric Power Distributions Systems: Decarbonization and Electrification
*Kolln J.T., J. Liu, S.E. Widergren, and R. Brown. 2023. Common Grid Services: Terms and Definitions Report Richland, WA: Pacific Northwest National Laboratory.
Anamika Dubey and Sumit Paudyal (2023), “Distribution System Optimization to Manage Distributed Energy Resources (DERs) for Grid Services”, Foundations and Trends® in Electric Energy Systems: Vol. 6: No. 3-4, pp 120-264. http://dx.doi.org/10.1561/3100000030
M. Kezunovic, A. Annaswamy, K. Baker, S. Brahma, K. Davis, A. Dubey, M. Hedman, J. Mitra, S. Oren, Chee-Wooi Ten, M. Saeedifard, R. Sioshansi, and Le Xie, “Grid at the Edge: Challenges and Opportunities,” Final Report, June 2021, Workshop on Research Directions for the Grid Edge.
A. Dubey, A. Bose, M. Liu and L N. Ochoa, “Paving the Way for Advanced Distribution Management Systems Applications: Making the Most of Models and Data,” IEEE Power and Energy Magazine, vol. 18, no. 1, pp. 63-75, Jan-Feb 2020.
Common Grid Service terms and the associated objectives*
How to unlock grid services from DERs/Grid-edge devices?
Technical challenge
-- Large-scale optimization and control
Grid Requires: Supply-Demand balance at all times
Grid services are designed to meet this requirement

## Slide 4: Optimizing Grid Operations
Example problem – Optimizing for grid operations for a specific grid-service.
Optimal power flow is an old problem. Classically solved using DC and AC power flow models for bulk grid systems. Current bulk grid markets use these optimizations.
What changed with grid-edge?
307,236 end-use customers with 160 high-voltage buses, 448 feeders*
Synthetic 2000-bus power system test case*
A. B. Birchfield, T. Xu, K. M. Gegner, K. S. Shetye and T. J. Overbye, "Grid Structural Characteristics as Validation Criteria for Synthetic Networks," in IEEE Transactions on Power Systems, vol. 32, no. 4, pp. 3258-3265, July 2017
Growing number of controllable resources
Simple rule-based control is not sufficient to achieve the primary goal of low-cost, reliable and resilient power
Given size and complexity, these systems are very hard to model and optimize
A. Dubey, A. Bose, M. Liu and L. N. Ochoa, "Paving the Way for Advanced Distribution Management Systems Applications: Making the Most of Models and Data," published in IEEE Power and Energy Magazine, vol. 18, no. 1, pp. 63-75, Jan-Feb 2020.
Notes: Grid problems have always been computationally challenging – so what has changed? How to scale examples? Operation/Coordination of Grid Services Problem OPF example from comparison paper?

## Slide 5
Specific Research Questions
How to unlock grid services from DERs/rid-edge resources? What kinds of broader challenges we are facing and how optimizing grid-edge can help?
What are the unique modeling and optimization challenges that require developing specialized algorithms for distribution systems?
What about planning problems? How and where to strategically place these resources to maximize their value?
When traditional optimization and control methods aren’t sufficient? How can we benefit from incorporating scientific and physics-informed Machine Learning (ML) methods?
How
Technical challenge -- Scalable modeling and optimization

## Slide 6: Grid-edge Coordination as Distribution-level Optimal Power flow Problem
A typical optimal power flow (OPF) problem
  min/max objective function
  subject to
  equality constraints
  inequality constraints
Objective function – energy efficiency, loss minimization, resilience
Equality constraints - power flow equations, device models, and network topology
Inequality constraints - thermal limits, voltage bounds, reactive power capabilities
Stochastic versions – capturing different uncertainties
Scalable and robust approaches to coordinate/operate heterogenous distributed resources for operational flexibility.
Anamika Dubey and Sumit Paudyal (2023), “Distribution System Optimization to Manage Distributed Energy Resources (DERs) for Grid Services”, Foundations and Trends® in Electric Energy Systems: Vol. 6: No. 3-4, pp 120-264. http://dx.doi.org/10.1561/3100000030

## Slide 7
Computationally tractable centralized algorithm1: iterative algorithms using approximation and relaxation
Mathematical decomposition to achieve scalability2: nodal decomposition with distributed computing for scalable nonlinear programming algorithms
Benchmarking studies of distribution OPF Algorithms4 and monograph summarizing state-of-the-art methods and applications of distribution-level OPF5
RL algorithms for fast/real-time optimization/operations
Imitation Learning: Use data to improve approximate (low-compute) optimization models for very fast decisions6
Solutions to ensure safety7 and address sim-to-reality gap
1R. R. Jha and A. Dubey, “Network-Level Optimization for Unbalanced Power Distribution Systems: Approximation and Relaxation,” IEEE Transactions on Power Systems, March 2021.
2R. Sadnan and A. Dubey, “Distributed Optimization using Reduced Network Equivalents for Radial Power Distribution Systems,” IEEE Transactions on Power Systems, Jan 2021.
3H. Ren, R.R. Jha , A. Dubey, “Extremum-Seeking Adaptive-Droop for Model-free and Localized Volt-VAR Optimization,” IEEE Transactions on Smart Grid, June 2021.
4R. R. Jha, A. Inaolaji, B. D. Biswas, A. Suresh, A. Dubey, S. Paudyal, S. Kamalasadan, "Distribution Grid Optimal Power Flow (D-OPF): Modeling, Analysis, and Benchmarking," IEEE Transactions on Power Systems, Oct 2022.
5Anamika Dubey and Sumit Paudyal (2023), “Distribution System Optimization to Manage Distributed Energy Resources (DERs) for Grid Services”, Foundations and Trends® in Electric Energy Systems: Vol. 6: No. 3-4, pp 120-264. http://dx.doi.org/10.1561/3100000030
6Gayathri Krishnamoorthy, Anamika Dubey, and Assefaw H. Gebremedhin, “Reinforcement Learning for Battery Energy Storage Dispatch augmented with Model-based Optimizer,” presented, IEEE SmartGridComm 2021, Aachen, Germany, 24-28 Oct. 2021
7Daniel Glover and Anamika Dubey, “Centralized Coordination of DER Smart Inverters using Deep Reinforcement Learning”, IEEE IAS annual meeting, 2023.
Summary of our work in this domain
Algorithms that leverage domain knowledge help improve performance

## Slide 8
Research Collaborations with PNNL
https://gridappsd-restoration.readthedocs.io/en/latest/
GridAPPS-D platform
Optimization of Grid-edge resources for Grid services - Manage active and passive devices by integrating data, measurement, and control for improved reliability, resiliency, efficiency.
Summary of Collaboration with PNNL
Opensource Advanced Distribution Management System – GridAPPS-D (Centralized and distributed coordination of grid-edge devices)
CITADELS – Advanced operations for networked microgrids (Distributed coordination of networked microgrids for resilience and bulk-grid support)
DOE Connected Community – Deploy distributed/layered coordination architecture using open-source distributed systems platform
DOE SETO RACER - Deploy and field demonstrate resilient restoration solutions using open-source distributed systems platform
Layered coordination architecture for distributed applications
OpenDSO/OpenFMB architecture
Technology development and field demonstration

## Slide 9
Python Distribution Optimal Power Flow Tool: DistOPF
Started at WSU as a part of AGI-related and PNNL-supported projects: Contributors from WSU and PNNL actively collaborating. Upcoming tutorial at premier PES conference.
Distribution OPF Sandbox: Provide higher level OPF user/developer to create new algorithms without reinventing the “Wheels” including ML-based control algorithms; support extensive benchmarking
Inviting contributors to develop, test and benchmark new algorithms
Contact: Rabayet Sadnan (rabayet.sadnan@pnnl.gov) and Nathan Gray (nathan.gray@pnnl.gov)

## Slide 10
Growing complexity of grid operations: Scalable simulation and optimization is key to study and operate the complex power grid.
System of systems – complexity
Changing nature and requirements of the grid at the edge interfacing
Scalability for interconnected T&D systems
https://www.wecc.org/
Existing Challenges and Next Steps
Promising directions: Distributed and parallel computing, Domain-specific approximations, Physics-informed learning
Notes: What is changing in the grid and what is needed to solve the emerging challenges? Scale of operational problem from Transmission to T&D?
Scalability challenges for more difficult class of problems: such as multi-period optimization, optimization under uncertainty, and multi-stage optimization
Existing Machine Learning Approaches are limited in providing guarantees for safe operation, and do not perform well under sim-to-real gap (Distribution models can be inaccurate, incorrect connectivity, topology, line parameters)

## Slide 11
Acknowledgments
Andrew Cannon, MS, SEL
Shiva Poudel, PhD, PNNL
Rahul Jha, PhD, ComEd
Gayathri Krishnamoorthy , PhD, NREL
Mohammed Ostadijafari , PhD, GE Vernova
Graduated
Research Group
Lusha Wang , PhD, Asst Prof, Univ of Alabama
Rabayet Sadnan, PhD, PNNL
Website: anamika-dubey.github.io
Abodh Paudyal, PhD, NREL
Srayashi Konar , PhD, GE Vernova
Surendra Bajagain, PhD, Dominion Energy

## Slide 12
Thank you
Contact: Anamika Dubey - anamika.dubey@wsu.edu +1 (509-335-1865)
Scholar -
‪Anamika Dubey‬ - ‪Google Scholar‬
Website - anamika-dubey.github.io