## Slide 1: Design of Fly Ash-Based Geopolymer Concrete-Filled FRP Tube Composite for Highly Durable and Environmentally Friendly Infrastructure
 | OPCC- Steel tube | OPCC- FRP tube | GPRC- Steel tube | GPRC- FRP tube
Mixture components | Cement, water, aggregate, steel tube, expanding agent | Cement, water, aggregate, FRP tube, expanding agent | Fly ash, water activators, steel tube, aggregate | Fly ash, water activators, FRP tube, aggregate
Compressive strength (MPa) | 60-100 | 40-100 | 60-100 | 50-100
Fire-resistance | high | high | high | high
Buckling resistance | high | high | high | high
Hauling and storage | Difficult | Easy | Difficult | Easy
Corrosion resistance | Low | / | Low | /
Xianming Shi, Ph.D., P.E.
Washington State University
Comparison between OPCC-steel tube, OPCC-FRP tube, GPRC-steel tube, and GPRC-FRP tube
Note: The variance of compressive strength of OPC/GPR concrete-tube composites mainly depend on the different strength of core filling materials.

## Slide 2
Sustainable and durable infrastructure
Geopolymer binder, including fly ash, silica fume, water glass, triisopropanolamine.
A small dosage of graphene oxide used to enhance microstructure
Fine/coarse aggregate
Lime and sodium sulfate used to adjust volume expansion
Treated rubber powder used to improve damping property
Research Plan and Goal
FRP tube used to restrict GPR concrete and improve it strength
Mechanical properties
Durability performance
Damping
properties
Numerical
simulation
GPRC-
FRP tube-
composite